THLOG
# Wiring
Pro Micro	KY-015
A2	Signal
VCC	Vcc	> Capacity
GND	Ground

# Components
## Overview
### Side

### Front

### Back

## Details
### Micro Controller
Name:	Pro Micro
Voltage:	5V
MCU:	ATmega32U4
Speed:	16MHz
USB:	Micro USB
Bootloader:	Arduino
Pinout:

Figure 1: 2019-06-24, https://images-na.ssl-images-amazon.com/images/I/81nOeGRzxPL._SL1500_.jpg
### DHT11 Sensor
Name:	KEYES KY-015
Voltage:	3.3V to 5.5V
Humidity:
Range:	20% to 90% RH
Accuracy:	±5% RH
Resolution	1% RH
Temperature:
Range:	0ºC to 50ºC
Accuracy:	±2ºC
Resolution:	1ºC
Pinout:

Figure 2: 2019-06-24, http://www.circuitbasics.com/wp-content/uploads/2015/12/DHT11-Pinout-for-three-pin-and-four-pin-types-2.jpg
### Screws
Name:	M3x25 or M3x30
Head:	Countersink
Nut:	ISO 4032
### Pin Header
Name:	single row female pin header (3 pin and 12 pin)
Height:	8mm (without soldering pins)
Spacing:	2.54mm
### Decoupling Capacity (optional)
Name:	Capacitor
Value:	100nF